## Slide 1
SHIVNAGAR VIDYA PRASARAK MANDAL'S
COLLEGE OF ENGINEERING, MALEGAON (BK)-BARAMATI.
BE Engineering
in
Electronics and Telecommunication Department

## Slide 2
In Vehicle Network Safety Established over CAN Communication protocol
OCTOBER 2024
PRESENTED BY: GADEKAR POURNIMA
SHAIKH ARBAJ
JAGTAP TUSHAR
HAJARE KIRAN
Guided By : Dr. N. A. Doshi

## Slide 3
Outline of Talk
Role Of Microcontrollers in Automotive Industry
ECU1 to ECU2: Use-case Diagram
System Block Diagram
Hardware Block Diagram
System Interface Diagram
Software Architecture Diagram
Sequence Diagram
CAN frame Types
Error Types
Implement & integrate CAN-stack on two different micro-controller
Define two CAN frames with E2E profile
E2E Protocols
References
Q&A Session

## Slide 4
Microcontrollers are used in a wide variety of automotive applications, including:
  Engine control
  Braking systems
  Airbag systems
  Transmission control
  Advanced driver assistance systems (ADAS)
  Infotainment systems
Role Of Microcontrollers in the Automotive Industry

## Slide 5
Micro Controllers Used in Automotive Industry

## Slide 6
ECU1 to ECU2: Use-case Diagram

## Slide 7
System Block Diagram

## Slide 8
Hardware Block Diagram

## Slide 9
System Interface Diagram:

## Slide 10
Software Architecture Diagram

## Slide 11
Sequence Diagram

## Slide 12
Sr.no | Frame | Roles of frame
1 | Data frame | This frame is used by the transmit unit to send a message to the receive unit.
2 | Remote frame | This frame is used by the receive unit to request transmission of a message that has the same ID from the transmit unit.
3 | Error frame | When an error is detected, this frame is used to notify other units of the detected error
4 | Overload frame | This frame is used by the receive unit to notify that it has not been prepared to receive frames yet
Frame Types and Roles of Each Frame

## Slide 13
Data Frame Format
SOF – Start of Frame, Identifier – Tells the content of message and priority
RTR – Remote Transmission Request, IDE – Identifier extension
DLC – Data Length Code Data – holds up to 8 bytes of data
CRC – “Cyclic Redundant Check” sum ACK – Acknowledge
EOF – End of Frame IFS – Intermission Frame Space.

## Slide 14
Remote Frame
RTR bit is Recessive and there is no Data

## Slide 15
Error Frame

## Slide 16
Error States of CAN Bus
Error Active
When the limit is below TEC (Transmit Error Counter) <127 and REC (Receive Error Counter) <127, an Error Active node will transmit Active Error Flags when it detects errors.

## Slide 17
Error States of CAN Bus
Error Passive
When any one of the two Error Counters raises above 127(TEC>127 and REC>127), the node will enter a state known as Error Passive.

## Slide 18
Bus Off
When the Transmit Error Counter raises above 255(TEC>255 and REC>255), the node will enter the Bus Off state. It happens when the CAN controller fails or at times of extreme accumulations of errors. In this case, the CAN controller disconnects itself from the CAN bus. As a result, that particular CAN node will get switched off from the CAN network; Resulting in no communication at all.

## Slide 19
Bit arbitration
Bit arbitration is a crucial process in the Controller Area Network (CAN) protocol. It refers to how nodes on a CAN bus determine which message will be transmitted when multiple nodes attempt to send data simultaneously.
The Arbitration Field, which determines the priority of the message when two or more nodes are contending for the bus.
Lower ID numbers indicate higher priority.

## Slide 20
Bit arbitration
Suppose you have two CAN nodes, Node A and Node B, both wanting to transmit a message on the CAN bus.
1. Start of Frame (SOF): The bus is initially in an idle state with all nodes in recessive mode (high-level, logic 1). When a node decides to transmit, it sends a dominant (low-level, logic 0) bit to signal the start of its message. This is called the Start of Frame (SOF) bit.
- Node A wants to transmit a message with an ID of 0x123.
- Node B wants to transmit a message with an ID of 0x456.

## Slide 21
Arbitration Field:
- Node A transmits its ID 0x123 (binary: 0001 0010 0011) bit by bit.
- Node B simultaneously transmits its ID 0x456 (binary: 0100 0101 0110) bit by bit.
During arbitration, the nodes compare the bits they are transmitting to the bits they observe on the bus. If at any point, a node sees a dominant bit when it intends to send a recessive bit, it backs off immediately. In this example, Node A transmits a dominant bit for the first arbitration bit (0) and Node B transmits a recessive bit. Node A wins arbitration for the first bit
Bit arbitration

## Slide 22
CAN stack means that these layers are designed as separate, interchangeable modules, each responsible for a specific set of functionalities.
This modular design allows for easier development, testing, and maintenance of the CAN stack, as each module can be developed and tested independently.
It also allows for flexibility in choosing different implementations for each layer, depending on the application’s requirements.
Implement & integrate CAN-stack on two different micro-controller

## Slide 23
Frame 1 for Data Transmission
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
Start of frame
Data Content
ID1
ID2
ID3
ID4
ID5
ID6
ID7
ID8
ID9
ID10
ID0
Requ. Remote
Arbitration Field
IDE Bit
Reserved
11
DL3
DL2
DL1
DL0
Control
4
DB7
DB6
DB5
DB3
DB4
DB2
DB1
DB0
Data
8
CRC Field
15
CRC14
CRC13
CRC12
CRC11
CRC10
CRC9
CRC8
CRC6
CRC7
CRC4
CRC2
CRC0
CRC3
CRC1
CRC5
1
1
1
1
CRC Delimiter
Ack. Slot Bit
Ack. Delimiter
EOF6
EOF5
EOF4
EOF3
EOF2
EOF1
EOF0
End of Frame
7
1
Complete CAN Frame
IFS2
IFS1
IFS0
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
Data Content

## Slide 24
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
Start of frame
Data Content
ID1
ID2
ID3
ID4
ID5
ID6
ID7
ID8
ID9
ID10
ID0
Requ. Remote
Arbitration Field
IDE Bit
Reserved
11
DL3
DL2
DL1
DL0
Control
4
DB7
DB6
DB5
DB3
DB4
DB2
DB1
DB0
Data
8
CRC Field
15
CRC14
CRC13
CRC12
CRC11
CRC10
CRC9
CRC8
CRC6
CRC7
CRC4
CRC2
CRC0
CRC3
CRC1
CRC5
1
1
1
1
CRC Delimiter
Ack. Slot Bit
Ack. Delimiter
EOF6
EOF5
EOF4
EOF3
EOF2
EOF1
EOF0
End of Frame
7
1
Complete CAN Frame
IFS2
IFS1
IFS0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
Data Content
Frame 2 for Data Reception

## Slide 25
E2E profile in CAN frames is to enhance the reliability of data transmission by adding checksum and sequence number checks.
This helps detect and mitigate errors that may occur during data transmission over the CAN bus, improving the overall robustness of the communication system.
E2E Data Frame:
  Frame Type: Data frame.
  Purpose: To transmit application data with added end-to-end checks for integrity and consistency.
  Structure: Contains the application data along with additional E2E checksum and sequence number fields.
  E2E Checksum: A checksum calculated over the entire data field to detect errors in the data.
  Sequence Number: A field that increments with each transmitted frame, allowing the receiver to detect missing or out-of-order frames.
E2E Error Frame:
  Frame Type: Error frame.
  Purpose: To notify the sender and other nodes of an error detected by the E2E checks in a received data frame.
  Structure: Contains the sequence number of the erroneous frame along with an error status code.
  Error Status Code: Indicates the type of error detected, such as checksum error or sequence number mismatch.
Define two CAN frames with E2E profile resp

## Slide 26
E2E Protocols: Freshness & Checksum
Freshness:
Freshness in E2E safety refers to ensuring that messages are current and not replayed from a previous communication session. It involves adding a time-based or sequence-based value to messages to prevent replay attacks.
Checksum:
A checksum is a value calculated from the data in a message that is used to detect errors or tampering during transmission. It helps ensure data integrity by verifying that the received message matches the transmitted one.
Image Source: https://www.wallarm.com/what/what-is-end-to-end-encryption

## Slide 27
References
Brayanov, N., and Stoynova, A. (2018). Multi-Microcontroller Emulation of Sensors, Actuators and Systems for Flexible Integration of Complex Devices. In 2018 41st International Spring Seminar on Electronics Technology (ISSE), pages 1-5.
Lin, Y., Conners, J., & Livengood, S. (2017, October). Assessing the use of open source microcontroller board for teaching engine sensing and communication in automotive laboratory. In 2017 IEEE Frontiers in Education Conference (FIE), pages 1-8.
H. Kopka and P. W. Daly, A study on the design and manufacture of HVAC Double Cylinder Motor for a car blower ,International Conference on Electrical Machines and Systems Nov 2009.
Z. M. Durovic and B. D. Kovacevic Control of heating, ventilation and air conditioning system based on neural network , 3rd ed. 7th Seminar on Neural Network Applications in Electrical Engineering, Sept 2004.

## Slide 28
THANKS

## Slide 29
Questions Please ?